## Slide 1
Virtual Sensor HIL Telemetry Engine
Abhisekh Routray
Reg. No. 2341018198

## Slide 2
Why I built this
The problem
Testing embedded code usually means real sensors and real wiring. And some faults, like a frozen sensor or a sudden spike, are hard (or unsafe) to repeat whenever you want.
My answer
Move the whole test bench into software: a Linux driver plus a C++17 app that act like a heated chamber.
What I set out to do
1
Produce temperature, humidity and pressure readings
2
Read them through a Linux driver or a simulator
3
Keep the chamber at a target with a PID controller
4
Spot spikes, stuck values and dropouts
5
Switch the heater off if it gets too hot, and show it all in a browser

## Slide 3
The big picture
Browser dashboard
Shows readings, sets targets, injects faults
C++ web server
Serves the page and a small JSON API
Control thread
Every 100 ms: read, check, run PID, drive heater
Sensor source
Simulator, or the /dev/vsensor0 driver
Shared state
A mutex keeps the target, fault mode and recent samples safe between threads.
One owner
Only the control thread touches the sensor. The web server just leaves commands.
Two modes
Simulator runs anywhere. Driver mode needs the kernel module loaded.

## Slide 4
A chamber that lives in software
How it behaves
The heater pushes the temperature up. Left alone, it slowly drifts back down to room temperature. Humidity dips a little as it warms, and pressure is simulated too.
25 °C
the ambient level it settles back to. It's a simplified model, not a measurement.
Faults I can switch on
1
Stuck
Output freezes at its last value
2
Spike
A +20 °C glitch on every 10th sample
3
Dropout
read() fails with an I/O error

## Slide 5
What happens every 100 ms
1
Pick up commands
A new target or fault mode from the browser.
2
Read the sensor
One sample from the driver or the simulator.
3
Check it
Is it believable? Spike, stuck, out of range?
4
Decide
PID on the last good temperature, unless it's over 100 °C.
5
Drive the heater
Send the output back out, 0 to 100%.
6
Publish and log
Update the dashboard data and write a CSV row.

## Slide 6
Not trusting every reading
PID heater control
8.0
Kp
0.4
Ki
1.0
Kd
Output stays between 0 and 100%. Anti-windup stops the integral from piling up while the heater is already at full power.
Three ways a reading gets rejected
1
Out of range
Below -40 °C or above 125 °C
2
Spike
Jumps more than 5 °C between samples
3
Stuck
Same value four times in a row
When a reading is rejected, the PID keeps using the last good one. Above 100 °C, the heater is cut to 0%.

## Slide 7
Talking to the kernel
One sensor frame
Timestamp and sequence number
Temperature in milli-degrees C
Humidity in milli-percent
Pressure in pascals
Heater percent and a fault flag
All integers, because kernel code avoids floating point.
Four ioctl commands
VS_IOC_SET_HEATER
Set heater output, 0 to 100%
VS_IOC_SET_FAULT
Pick none, stuck, spike or dropout
VS_IOC_RESET
Reset the device
VS_IOC_GET_STATS
Read reads, faults and dropouts

## Slide 8
What you see in the browser
On the dashboard
1
Live temperature, humidity and pressure
2
Change the target temperature
3
Trigger a spike, stuck or dropout fault
4
Watch the event log fill up as it happens
Under the hood
GET /api/data
GET /api/setpoint?value=55
GET /api/fault?mode=spike
Every sample also lands in telemetry.csv:
seq, temp_c, hum_pct, press_pa, heater_pct, setpoint_c, anomaly

## Slide 9
Try it yourself
Simulator mode
make
./build/bin/hil_server --mode sim
# then open http://localhost:8080
make test
make itest
Ctrl+C stops it. No kernel module needed.
Driver mode
make driver
./scripts/load_driver.sh
./build/bin/hil_server --mode driver
./scripts/unload_driver.sh
Needs kernel headers that match your running kernel.

## Slide 10
Did it work? The numbers
12 / 0
integration checks passed / failed
59.95 °C
reached for a 60 °C target
36%
heater output once it settled
100 ms
control cycle at a fixed rate
What I checked
Unit tests cover the PID, the health checker and simulator faults. Integration tests use curl against the running app.
Worth being honest about
These are simulated results, not physical measurements. Driver mode still needs its own run on a matching Linux kernel.

## Slide 11
Where it falls short, and what's next
Today's limits
Simplified chamber model
One virtual sensor device
No login or encryption, so keep it on localhost
Ideas for next
Real sensors over I2C or SPI
Multiple devices and sensor models
Live dashboard updates and long-term storage
Configurable PID settings

## Slide 12
Thank you
Abhisekh Routray
Reg. No. 2341018198